## Slide 1: HPC/HTC vs. Cloud Benchmarking An empirical evaluation of the performance and cost implications
Kashif Iqbal - PhD
Kashif.iqbal@ichec.ie
ICHEC, NUI Galway, Ireland
With acknowledgment to Michele Michelotto – INFN for their kind support for the HTC Benchmarking + Resources

## Slide 2: Outline
Benchmarking - Why, which benchmark?
HPC and HTC Benchmarking
  Benchmarks (NPB, HEPSPEC06)
  Environment Setup
  Results
Concluding Remarks

## Slide 3: Overview
Rationale
  Diverse computing infrastructures (HPC. HTC, Cloud)
  Diverse workloads (SMEs, academics, app. Domains)
Methodology
  System benchmarking for:
    Comparison of HPC and HTC systems vs. Cloud offerings
    Comparison of parallelism techniques (e.g. MPI/OMP)
      ***To calculate the performance variation factor***
  For Cost analysis and infrastructures comparison
    Performance overhead as indirect costs
    Inclusion of an additional weight factor in the cost model

## Slide 4: Scope
What we are not doing?
  Benchmarking individual components (e.g. memory, network or I/O bandwidth)
Why?
  Because resources cost money
  Aim is to compare HPC, HTC and Cloud infrastructures to identify ranges for performance variations

## Slide 5: Benchmarks
LINPACK – Top 500
SPEC06 – CPU intensive benchmark
  HEP-SPEC06 (for HTC vs. Cloud instances)
HPC Challenge (HPCC)
  Linpack, DGEMM, STREAM, FFT…
Graph 500
MPPtest – MPI performance
NAS Parallel Benchmark (NPB)
  (for HPC vs. Cloud HPC instances)

## Slide 6: NAS Parallel Benchmark
Open-source and free CFD benchmark
Performance evaluation of commonly used parallelism techniques
  Serial, MPI, OpenMP, OpenMP+MPI, Java, HPF
Customisable for different problem sizes
  Classes S: small for quick tests
  Class W: workstation size
  Classes A, B, C: standard test problems
  Classes D, E, F: large test problems
Performance metric – Kernel execution time (in sec)

## Slide 7: NPB Kernels
Kernel | Description | Problem Size | Memory (Mw)
EP | Monte Carlo kernel to compute the solution of an integral – Embarrassingly parallel | 230 random-num pairs | 18
MG | Multi-grid kernel to compute the solution of the 3D Poisson equation | 2563 grid size | 59
CG | Kernel to compute the smallest eigenvalue of a symmetric positive definite matrix | 75000 no. of rows | 97
FT | Kernel to solve a 3D partial difference equation using an FFT based method | 512x256x256 grid size | 162
IS | Parallel sort kernel based on bucket sort | 225 no. of keys | 114
LU | Computational Fluid Dynamics (CFD) application using symmetric successive over relaxation | 1023 grid size | 122
SP | CFD application using the Beam-Warming approximate factorisation method | 1023 grid size | 22
BT | CFD application using an implicit solution method | 1023 grid size | 96
Notes: Mw demonstrates memory requirements
The unit Mw refers to one million 64-bit words

## Slide 8: Cloud Cluster Setup
EC2 instance management
  StarCluster Toolkit
    http://web.mit.edu/star/cluster/
    StarCluster AMIs – Amazon Machine Image
      Resource manager plugin
Login vs. compute instances
  EC2 small instance as login node
  File system shared via NFS across nodes

## Slide 9: Cloud vs. HPC
 | Amazon EC2 | Stokes HPC
Compute Node | 23 GB of memory, 2 x Intel Xeon X5570, quad-core “Nehalem” (8 cores X 4 Nodes) | 24 GB memory, 2 x Intel Xeon E5650, hex-core “Westmere” (12 cores X 3 Nodes)
Connectivity | 10 Gigabit Ethernet | ConnectX Infiniband (DDR)
OS | Ubuntu, 64-bit platform | Open-SUSE, 64-bit platform
Resource manager | Sun Grid Engine | Torque
Compilers & libraries | Intel C, Intel Fortran, Intel MKL, Intel MVAPICH2 | Intel C, Intel Fortran, Intel MKL, Intel MVAPICH2
Non-trivial to replicate runtime environments
Large variations in performance possible
Logical vs. Physical cores
  HT/SMT – Hyper or Simultaneous Multi-Threading (i.e. 2 X Physical Cores)
Notes: HT Enabled on both infrastructures

## Slide 10: NPB – MPI
The average performance loss ~ 48.42% (ranging from 1.02% to 67.76%).
BT and SP using 16 cores, rest using 32 cores (22 runs)
Chart: NPB3.3-MPI - Class B
| BT | CG | EP | FT | IS | LU | MG | SP
Stokes HPC | 39.341 | 6.084 | 1.4945 | 6.962 | 0.62045 | 15.4872 | 1.5486 | 32.751
Amazon EC2 | 82.827 | 18.504 | 4.0018 | 18.695 | 1.8764 | 31.685 | 1.5645 | 42.678

## Slide 11: NPB - OpenMP
The average performance loss ~ 37.26% (ranging from 16.18 - 58.93%
8 cores with 8 OMP Threads (22 runs)
Chart: NPB3.3-OMP -Class B
| BT | CG | EP | FT | IS | LU | MG | SP | UA
Stokes | 41.425 | 17.448 | 5.408 | 9.8118 | 0.5518 | 34.541 | 1.665 | 38.235 | 58.0327
EC2 | 63.234 | 28.344 | 6.694 | 11.706 | 1.0159 | 92.213 | 2.907 | 46.122 | 141.2777
Time in Seconds

## Slide 12: Cost
720 hours @ 99.29 USD 
  ~100 % utilisation
  Compute cluster instance @ $1.300 per Hour
  Small instance @ $0.080 per Hour
Other useful facts:
  On-Demand instances
  Overheads (performance, I/O, setup)
  Data transfer costs and time

## Slide 13: HEPSPEC Benchmark
HEP Benchmark to measure CPU performance
  Based on all_cpp bset of SPEC CPU2006
  Fair distribution of SPECint and SPECfp
  Real workload
  Performance Metric: HEPSPEC Score
32-bit binaries
  Can be compiled using 64-bit mode ~ for better results

## Slide 14: Benchmark Environment
 | Amazon EC2 | HTC resource at INFN
Compute Nodes | Medium: 2 ECU Large: 4 ECU XL: 8 ECU M3 XL: 13 ECU M3 2 XL: 26 ECU 1 ECU = 1.0-1.2 GHz | Intel(R) Xeon(R) CPU E5-2660 @ 2.2 GHz, 2 X 8 cores, 64 GB memory AMD Opteron 6272 (aka Interlagos) @ 2.1 GHz, 2 X 16 cores M instance Single-core VM L instance Dual-core VM XL Instance Quad-core VM M3 XL Instance Quad-core VM M3 Double XL Instance Eight Core VM
OS | SL6.2, 64-bit platform | SL6.2, 64-bit platform
Memory | 3.75 GB, 7.5 GB and 15 GB | 64 GB for both Intel and AMD
Hyper-Threading | Enabled | Enabled (for Intel) ~ 32 logical cores
Compilers | GCC | GCC
Notes: HT Enabled on both infrastructures (except Opteron)

## Slide 15: Benchmark Variations
Bare-metal vs. EC2 imply:
  *Cloud migration performance implications*
1 VM vs. Bare-metal:
  *Virtualisation effect*
n VMs + 1 loaded (HS06) vs. Bare-metal:
  *Virtualisation + multi-tenancy effect with minimal workload* - Best Case Scenario!
n VMs + n loaded
  *Virtualisation + multi-tenancy effect with full workload* - Worst Case Scenario!
Notes: Another possible variation could be the resource over-commitment effect
Will touch upon this in the later part of my presentation

## Slide 16: HS06 for Medium
SPEC score < with the > no. of VMs
Virtualisation + Multi-Tenancy (MT) effect on performance ~ 3.28% to 58.48%
47.95% Performance loss for Cloud migration
HS06 Score
Chart: 
| Bare Metal | 1 VM | n VMs + Minimal load | n VMs + Fully loaded
HTC | 21.94 | 21.22 | 19.41 | 9.11
EC2 | 11.42 | 11.42 | 11.42 | 11.42
No. of VMs = 32
Amazon EC2 - Possible variations
1 VM + idle – Unlikely in EC2
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!
NGIs – Possible variations
Bare Metal – NGIs current
1 VM + idle
N VMs + minimal load Future
N VMs + Fully loaded
Notes: 32 Signle Core VMs
Percentages calculated as follows: 100 – (21.22/21.94 x 100) = 3.28%

## Slide 17: HS06 for Medium
Virtualisation + MT effect on performance ~ 3.77% to 47.89%
18.19 Performance loss for Cloud migration
HS06 Score
Chart: 
| Bare Metal | 1 VM | n VMs + Minimal load | n VMs + Fully loaded
HTC | 13.26 | 12.76 | 11.73 | 6.91
EC2 | 11.42 | 11.42 | 11.42 | 11.42
No. of VMs = 32
NGIs – Possible variations
Bare Metal – NGIs current
1 VM + idle
N VMs + minimal load Future
N VMs + Fully loaded
Amazon EC2 - Possible variations
1 VM + idle – Unlikely in EC2
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!
Notes: - 32 Single Core VMs

## Slide 18: HS06 for Large
Virtualisation + MT effect on performance ~ 9.49% to 57.47%
Note the minimal effect on performance with > no. of VMs
58.79% Performance loss for Cloud migration
HS06 Score
Chart: 
| Bare Metal | 1 VM | n VMs + Minimal load | n VMs + Fully loaded
HTC | 44.04 | 39.86 | 40.67 | 18.73
EC2 | 18.15 | 18.15 | 18.15 | 18.15
NGIs – Possible variations
Bare Metal – NGIs current
1 VM + idle
N VMs + minimal load Future
N VMs + Fully loaded
Amazon EC2 - Possible variations
1 VM + idle – Unlikely in EC2
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!
No. of VMs = 16
Notes: - 16 dual core VMs

## Slide 19: HS06 for Large
Virtualisation + MT effect on performance ~ 9.04% to 48.88%
30.75% Performance loss for Cloud migration
HS06 Score
Chart: 
| Bare Metal | 1 VM | n VMs + Minimal load | n VMs + Fully loaded
HTC | 26.21 | 23.84 | 23.29 | 13.4
EC2 | 18.15 | 18.15 | 18.15 | 18.15
No. of VMs = 16
Amazon EC2 - Possible variations
1 VM + idle – Unlikely in EC2
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!
NGIs – Possible variations
Bare Metal – NGIs current
1 VM + idle
N VMs + minimal load Future
N VMs + Fully loaded
Notes: Dual core VMs

## Slide 20: HS06 for Xlarge
Virtualisation + MT effect on performance ~ 8.14% to 55.84%
Note the minimal effect of > no. of VMs
46.21% Performance loss for Cloud migration
HS06 Score
Chart: 
| Bare Metal | 1 VM | n VMs + Minimal load | n VMs + Fully loaded
HTC | 82.58 | 75.86 | 74.75 | 36.47
EC2 | 44.42 | 44.42 | 44.42 | 44.42
No. of VMs = 8
NGIs – Possible variations
Bare Metal – NGIs current
1 VM + idle
N VMs + minimal load Future
N VMs + Fully loaded
Amazon EC2 - Possible variations
1 VM + idle – Unlikely in EC2
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!

## Slide 21: M3 X-Large
Virtualisation + MT effect on performance ~ 18.24 – 55.26
43.37% Performance loss for Cloud migration
Chart: 
| Bare Metal | 1 + 3 VMs | 4 HS06
HTC | 82.58 | 67.52 | 36.12
EC2 | 46.77 | 46.77 | 46.77
Amazon EC2 - Possible variations
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!
NGIs – Possible variations
Bare Metal – NGIs current
N VMs + minimal load
N VMs + Fully loaded
No. of VMs = 8

## Slide 22: M3 Double X-Large
Virtualisation + MT effect on performance ~ 8.81 – 54.98%
37.79% Performance loss for Cloud migration
Chart: 
| Bare Metal | 1 + 3 VMs | 4 HS06
HTC | 150.38 | 137.13 | 67.71
EC2 | 93.54 | 93.54 | 93.54
Amazon EC2 - Possible variations
N VMs + minimal load – Best-case!
N VMs + Fully loaded – Worst-case!
NGIs – Possible variations
Bare Metal – NGIs current
N VMs + minimal load
N VMs + Fully loaded
No. of VMs = 4

## Slide 23: Interesting Finding
Over-commitment of resources vs. Cost effectiveness
  That is more reasonably why 1 ECU = 1.0-1.2 GHz 2007 Xeon or Opteron!!
Chart: 
| Bare Metal | 1 + 3 VMs | 4 HS06
No Overcomitment | 150.38 | 136.86 | 74.03
No Overcomitment | 150.38 | 135.03 | 72.24
Overcomitment | 150.38 | 137.13 | 67.71
Memory: 28GB of 64GB
Memory: 48GB of 64GB
Memory: 120GB of 64 GB
Notes: Overcommitting only for the memory resource (2.42% when we increase memory assignment, 8.54% when we overcomitt only the memory resource
We did not study (explicitly) the effect of overcomittment on performance

## Slide 24: Conclusions – HPC vs. EC2
As expected a purpose built HPC cluster outperforms EC2 cluster for same number of OMP threads
  Average performance loss over all NPB tests: ~37%
Similarly so for when comparing 10GigE versus Infiniband networking fabrics
  Average performance loss over all NPB test: ~48%
Even at a modest problem size the differences in performances between systems is highlighted.

## Slide 25: Conclusions – HTC vs. EC2
Virtualisation overhead is much less than the Multi-Tenancy effect
  What others are running will have a direct effect!
Standard deviation with pre-launched VMs in EC2 is significantly low!
  Results with M3 L instance: 46.92, 46.61, 47.79
HS06 Scores variations in the order of 40-48%

## Slide 26: Thank you for your attention!
Questions??
kashif.iqbal@ichec.ie