## Slide 1: Configuration management tools used at EGI (overview of survey)
EGI.eu Operations

## Slide 2: Why the survey?
Yaim configuration of grid services for an homogeneous set of variables
  Future support of Yaim core is uncertain…
Some EMI services are moving away from yaim to specific configuration files/scripts
  Uniform configuration parameters across services are desirable
  Configuration management templates can re-use parameters, which are shared between services

## Slide 3: Survey summary
Survey opened: Jan 28th, closed: Mar 24th
  Circulated directly among sites
  87 answers
Questions:
  Size of the sites: number of services / number of worker nodes
  Configuration management tools used (or evaluated)
    Pros and cons
  Modules used for grid services and OS
    Developed by the site/NGI/others

## Slide 4: Is the site using configuration management tools?
3 - Home made solutions
2 – Ansible
1 - cobbler
1 - xcat
54
Evaluating?
- 18 not yet chosen
- 6 Puppet

## Slide 5: Number of services deployed vs conf. tool used
# of services deployed | Quattor | Puppet | Chef | CFengine | Total sites
Less than 10 | 8 | 8 | 0 | 3 | 59
Less than 30 | 5 | 7 | 1 | 3 | 29
Less than 50 | 0 | 0 | 0 | 0 | 1
More than 50 | 3 | 3 | 1 | 0 | 8

## Slide 6: Pros and cons
Quattor (15)
  grid services templates available, knowledge base in the grid community (QWG)
  Small community, steep learning curve, complicated to update
Puppet (16)
  Huge community, well documented, many plugins available
  Lack of grid modules, initial configuration takes time
Chef (2)
  Reliable, mainstream, cloud interfaces available
  Not widely used in the infrastructure, doesn’t configure O.S.
CFEngine (4)
  Flexible, easy alteration of config files
  CFv2 CFv3 difficult migration

## Slide 7: Custom modules for Grid 1/2
Do you use specific modules developed for the grid services?
Chart: 
| No,used only for the operating system configuration | Yes, we have developed the modules in our site | Yes, we have developed the modules in our NGI | Yes, but developed by other partners
Puppet | 4 | 11 | 3 | 5
Quattor | 6 | 6 | 1 | 7
CFEngine | 4 | 3 | 0 | 0
Chef | 0 | 2 | 1 | 1

## Slide 8: Custom modules for Grid 2/2
Quattor: generally calling Yaim
  Customizations for local monitoring, bugs workaround and fine tuning
Puppet: most of the sites are using modules calling Yaim
  CERN is working on Yaim-free modules for: WN, CREAM, VOMS, MyProxy, BDII, DPM/LSF, Slurm, CVMFS, Argus, FTS, LFC
  VU-MIF-LCG2, Yaim-free configuration for BDII
  T3_CH_PSI, configuration modules for dCache and ARC
Chef: Using Yaim

## Slide 9: Summary
No single configuration tool good for all the grid sites
Puppet is taking the lead
  Growing user community within EGI
    Already a big user community worldwide (true also for other tools)
  Big site (CERN) working on a set of templates (master/masterless)
    Lot of templates, but not all the products are covered
  Coordination work starting within an Hepix working group

## Slide 10: Future actions
Cooperate with the Hepix WG
Facilitate sharing of work done by site managers/NGIs  discussion forum
  Re-use the modules already available (avoid duplication)
  Collaboration on testing
  Fill in the gaps, focusing on the missing services (yaim-free modules)