## Slide 1: Towards the Big Data Strategies for EISCAT-3D
Yin Chen
ChenY58@cardiff.ac.uk

## Slide 2: Opportunities for new Research
EISCAT-3D New Measurement Capabilities
  Instantaneous, adaptive control of beam positions
  Simultaneous multiple beams/interlaced beams
  High-resolution coding of polarisation, phase and amplitude
  Aperture synthesis imaging – small-scale 3D imaging(sub-beam-width)
  Multi-beam volume imaging – large-scale 3D imaging
  Full-profile vector measurements – large/small-scale 3D vector imaging
  High-speed object tracking
      * Estimated for 3 MW Tx: improvement at least x 10 better
Notes: motivations

## Slide 3: Opportunities for new Research
  EISCAT-3D e-Infrastructure capabilities
    Real-time data access
    Virtual observation
    Support long-tail scientists
      Search through all levels of data, e.g.,
        Find specific signature at all levels
        Plasma features, meteors, space debris, astronomical features
      Search for other ISR data resources
      User specifying data analysis/processing
    New Applications, e.g.,
      Space weather
      Visualisation

## Slide 4: The Big Data Challenges in EISCAT-3D
3 +1 Vs
      Volume.
        5PB/year in 2018, 40PB/year in 2023
        Operate for 30 years, data products to be stored for > 10 years
      Velocity.
        Each antenna : 120MB/s
        160 * antenna group (100 antennas): 2 Gbit/s/group
        5* Ringbuffer: each 125 TB/h
      Variety.
        Measurements: different versions, formats, replicas, external sources ...
        System information: configuration, monitoring, logs/provenance ...
        Users’ metadata/data: experiments, analysis, sharing, communications …
      Value.
        Meaningful insights that deliver analytics/patterns from deep, complex analysis based on machine learning, statistical modelling, graph algorithms ...
        Go beyond traditional approaches to the space science
Notes: challenges

## Slide 5: EISCAT-3D Data Acquisition
5 Types of data
  Raw antenna (group) data (10 PB/day)
  Voltage beam formed data (10 PB/year)
  Correlated products (1 PB/year)
  Fitted data (1GB/year)
  (User) Specialised Products

## Slide 6
Each antenna
      30 Msamples/s (120MB/s)
Antenna group (core site)
      Computes a number of (broad) beams from a small number of antennas (FPGAs)
      100 antennes → 1 beam 2 polarisations
            At 30 MHz IQ this is 32 * 30 * 2 = 2 Gbit/s/group
      These data are stored in a ringbuffer
            160 groups → 125 TB/h
EISCAT-3D Data Acquisition

## Slide 7: EISCAT-3D Data Acquisition
2nd stage beamforming
    160 antenna groups → 100 beams
          Decimation to 1MHz→ 200 Gflop/s
          Continuing sampling 32bit words (I/Q)
            100*1e6*2*32 → 1GB/s
            2* 10MHz bands correlated data → 2GB/s
            In total 10TB/h to be stored in archive
Lag profile inversion
    2-3 Tflops/s/beam
Total 5-10 + beams*(2-3) Tflops
    8-13 Tflops for 1 beam
    200-300 Tflops/s for 100 beams

## Slide 8
One want occasionally do offline work on the ringbuffer data
    Need transfer to HPC
        Link or physical transport
            1Tb/s → 1 month, better to do the calcs on-site?
        125 TB/h * 1 day → 3 PB
        In total ~10PB storage at HPC (72h data)
    HPC computing
        Higher resolutions (spatial and time)
        4Pflop/s*24h → 10⁵ Pflop
EISCAT-3D Data Acquisition

## Slide 9: EISCAT-3D Data Curation
Tire 1
Tire 0
Data Acquisition

## Slide 10: EISCAT-3D Tire 0 Curation
Existing EISCAT
  Small, EISCAT archive (1981-2013) 60TB
EISCAT_3D 1st stage (2018)
  Moderate, EISCAT archive 1PB/year
  2-3 Mirrors (North + South Europe+Japan)
  Analyis software + Search engines
  HPC for detailed studies/developments
  Storage 1PB, 1Pflop/run
EISCAT_3D 2nd stage (2023)
  High, EISCAT archive 10PB/year
  HPC, Storage 10PB, 10 Eflop/run

## Slide 11: EISCAT-3D Tire 1 Curation
Data Access & Processing
Tire 0
Tire 1

## Slide 12: EISCAT-3D Tire 1 Curation
Data staging
Long-term perservation
Security service, e.g., single sign-on, authentication, authorisation
Large scale virtualization of data/compute center resources to achieve on-demand compute capacities
Computing sites and workload management
Metadata service
File catalogue, application registration
Safe Replication service, e.g., dynamic data streams
Simple Store, e.g., drop-box like service for data
Semantic annotation services
A web based science gateway system

## Slide 13: EISCAT-3D Data Access & Processing
Unlock the hidden-value of the big data
    Discovery & Access
      Intelligent filter
      Signature search, similarity, pattern
      Connecting big data with existing research analysis
      To support discovery of “unknowns”
      Metadata-based
      Integration of other resources
    Processing
      Statistical analysing, correlation process
      Visualisation
      Domain Applications, e.g. , space weather service

## Slide 14: EISCAT-3D Data Access & Processing
A digraph will be provided here …

## Slide 15: Objective 1: Support EISCAT Science Community
Real-time data access
Community driven design
Virtual research environments
Support Long-tail scientists
Global data sharing and integration

## Slide 16: Objective 2: Common Services for Big Data
Identify common requirements, challenging issues, state-of-the-art design experiences
    LOFAR
    LHC
    SKA
    The Pierre Auger Observatory
    Cherenkov Telescope Array
Advance existing technologies
  Proof of concepts /prototypes of data infrastructure-enabling software
  Support to the evolution of EGI
  EUDAT:
    Common storage, computing, metadata services to large research communities (typically ESFRI)
    Robust solutions to replicate and optimize data access.

## Slide 17: Objective 3: Training of Data Scientists
The 4th paradigm for science
A new data-centric way of conceptualising, organising and carrying out research activities
New approaches to solve problems that were previously considered extremely hard/ impossible to solve
This will lead to serendipitous discoveries and significant scientific breakthroughs

## Slide 18: Participating Organisations
Cardiff University
CERN
CSC
  CSC provides IT support and resources for academia and research institutes.
  CSC is a part of the Finnish national collaboration on building EISCAT-3D in coordination with the other member states.
  Planned role to provide capacity and expertise in data management, HPC/Cloud services and connecting the EISCAT stations with high-speed networks.
  CSC’s modular Data Center in Kajaani offers >2200 Tflops HPC capacity in 2014.
EGI
EISCAT
EUDAT
University of Edinburgh