## Slide 1: Workflow of Tsunami Inversion
Apr 13, 2015

## Slide 2
Choose
inversion area
Make unit source
Run COMCOT for each unit source
Input:
*bathymetry.xyz
(bathymetry data)
*comcot.ctl
(control file)
*ini_surface.dat (initial water surface data, 1 meter for each unit source) *ts_location.dat (tidal station location, at least one, three is better)
Get initial water surface
Input 1obs. data, tidal station records with time serial and 2COMCOT result, time serial records. Then use least square and smoothing method to get inverse initial water surface.
Workflow and Data for
Tsunami Inversion
Decompose into Unit Sources
create initial surface data (ini_surface.dat) by COMCOT.
Input inversion area map then split it to unit source and make 1 meter water height to each unit source.

## Slide 3
Estimate the possible epicenter.
Creating time serial record of water surface height by max water height.
Do tsunami inversion by fictitious data.
If Observed Time Series Data Is Missing, Only One Max Wave Height Could be Found