## Slide 1: Collaborative scientific platforms for accessing, processing and validation of biodiversity observation and biosensor data. Francisco Hernandez, Joram Declerck, Klaas Deneudt, Cis Hernandez
Lifewatch - EGI engage May 2015

## Slide 2: Outline
Lifewatch
EGI - ENGAGE
  Collaborative scientific platform
    Biosensors
    Challenges
    Status
  Virtual labs and research environments
Progress

## Slide 3: Lifewatch infrastructure
European research infrastructure, ESFRI roadmap
Study of biodiversity and ecosystems
Access to realtime data
Biosensor networks
BIG data, inline data processing
More info : http://www.lifewatch.eu
Example VRE : http://marine.lifewatch.eu/
Belgian contribution: http://www.lifewatch.be

## Slide 4: Biosensors
Biological sensors that enable observations at space and time scales relevant to organisms behavior, physiology and life history
  Optics, Acoustics, Genetics, GPS
Discrete => continuous
Delayed mode => real-time

## Slide 5
http://www.lifewatch.be/en/sensors

## Slide 6: Zooscan
High resolution flatbed scanner for water samples
Digital storage and processing of zooplankton samples -> taxonomic composition and abundance
Image acquisition: 2400-4800 dpi
Data generation: +/- 4 GB/sample; 432 Gb/year
Analysis: pattern recognition software (Plankton Identifier [Tanagra], ZooImage [R], …)

## Slide 7: Video Plankton Recorder (VPR)
Real-time underwater digital camera system + strobe
Rapid quantification of plankton taxonomic composition and abundance
Image acquisition: 30 frames/second of 7.2 ml image volume
Data generation: +/- 10GB/h (at 150kb/image) , 1.5M files / h
Analysis: pattern recognition software (Visual Plankton software [Matlab])

## Slide 8: Flow cytometer
Laser based instrument for particle detection and characterisation in fluids
Counting and characterisation of phytoplankton particles -> taxonomic composition and abundance
Image acquisition: particle scattering + fluorescence
Data generation: +/- 200 MB/sample; 1Tb/year
Analysis: clustering software (Easyclus [Matlab], FCM [R], …)

## Slide 9: Acoustic fish telemetry
Acoustic fish tag tracking
Studying distribution, migration and habitat use
Data generation: 25 MB/month
Analysis: GIS mapping & visualization (CartoDB), behaviour analysis (Matlab, Python)

## Slide 10: Multibeam echosounder
Acoustic high resolution depth sounding sonar
Bathymetry and sediment typology
Data generation: sediment 10Gb; water column 100Gb/day
Analysis: data cleaning and validation, chart creation, deriving sediment typology (CARIS, Fledermaus)

## Slide 11: Sediment profiler imaging
Digital Sediment Profiling Camera
Vertical cross section of the sediment/water interface
Image acquisition: 24.1 Mpixel images of 320 cm2 of sediment
Data generation: 1Gb/image; 130 Gb/year
Analysis: Image pattern recogition software, relating to benthic communities

## Slide 12: Acoustic bat recorder
Ultrasound detection and recording
Sound acquisition: 500 kHz with 16 Bit amplitude resolution
Data generation: 1 MB/per second of sound recording; 0.5 Gb/night
Analysis: Call detection and recogition software

## Slide 13: Bird tracking with GPS
Tracking of large birds with GPS tags developed by UvA-BiTS
Studying migration and habitat use
GPS position every 10min, 70 birds, soon > 100
Data generation: 3G/year (Flemish LifeWatch), multiple GB/year (UvA-BiTS)
Analysis: GIS mapping & visualization, behaviour analysis (Matlab,Python,R)

## Slide 14: Challenges
Biosensor
  buy and install equipment: sensors, winches, antennas
  technical calibration, raw signal processing, vendor softw.
IT
  real-time data transfer, storage, processing
Biology
  sensor output -> biodiversity parameters
  aggregating, combine data, models & predictions, visualization, sharing, validation,…

## Slide 15: Doctoral studies on sensor use and application
  4 PhD’s at Ghent University
  Started October 2014
  Work on :
    Standard operation procedures
    Algorithms for translation of sensor output to biodiversity parameters on abundance and distribution of taxa
    Recommendations on optimization and upgrade of the infrastructure
    Applications of the infrastructure in biodiversity and ecosystem studies

## Slide 16: Collaborative platform for sensor data processing and analysis
Flowcytometer
Sensor network
Fish tags
Bird tracks
Sensor data
Archive
?
R, Java, Python, Rstudio, Rshiny
Scripts, workflows, algorithms
Scientific data
Rsync
Calibration data
Processing network
Species identifications, field observations, crowd sourcing
Science community
VPR
Bird Radar
Benthic img
Fish sonar
Remote sensing
In situ habitat obs.
Bird video
Hydrophones
eDNA
Postgis, Geoserver
LW ICT core
FedCloud
?

## Slide 17
Infrastructure | Status
Bird GPS tracking network + web cams | 3 base stations installed and operational 70 birds with GPS
Flow Cytometer | Installed on RV Simon Stevin and operational
Multi beam | Installed on RV Simon Stevin and operational
Acoustic bat detectors | Test installation installed. Offshore installation in preparation
ZooScan | Installed in MSO lab and operational
Video Plankton Recorder | To be installed July 2014
Sediment Profile Imaging | Installed on RV Simon Stevin and operational
Acoustic fish telemetry | 40 fishes tagged, 51 receivers installed, data for >2 years
Environmental DNA | Several species of fish and jellyfish under investigation

## Slide 19
mongoDB network

## Slide 20: File management

## Slide 21: Progress
Ongoing testing with ICT Core facilities: IFCA, EGI ENGAGE
Create virtual servers
  on fedcloud : problem with OCCI
  on IFCA / LW servers : on going / tickets
  R, R studio server, Rshiny : at VLIZ
  PostGIS, geoserver : at VLIZ
Set up data transfer
  from ship & stations to IFCA : daily Rsync operational
  from VLIZ geoserver to IFCA
  manage storage capacity
Set up user interfaces for scientists
  VLIZ users : started
  external users
  manage resources: user data, algorithms, scripts, models, …

## Slide 22: Lifewatch virtual labs to ICT core
Meeting in Amsterdam
Collect and present existing virtual labs
  Lifewatch Marine Virtual Research Environment (VRE) : done
  VRE for terrestrial & other thems: started
Upscale virtual lab components using LW ICT core
  Environmental layers, Species occurence data
  BIOVEL portal , Biodiversity catalogue
  Taxonomic, Biostatical & Modelling webservices
http://marine.lifewatch.eu/

## Slide 23: More info
Lifewatch website http://www.lifewatch.eu
Marine VRE : http://marine.lifewatch.eu/
Belgian contribution: http://www.lifewatch.be
Flanders Marine Institute : http://www.vliz.be