## Slide 1: Early Warning System by Forecast Fire Danger Rating System of Thailand and Upper ASEAN and Forest Fire Control in Thailand
Veerachai Tanpipat, D.Eng.
veerachai@haii.or.th &
iamtanpipat@hotmail.com
Disaster Mitigation Workshop at APAN43 on 15-16 Feb 2017
https://worldview.earthdata.nasa.gov/

## Slide 2: Contents
What is Early Warning System for Forest Fire?
What is Fire Danger Rating System (FDRS)
Global Fire Early Warning System
ASEAN FDRS System
Forecast Thailand and Upper ASEAN FDRS
6 things that Forest Fire Information System needs to include
Forest Fire Decision Supporting and Management System (FFDSMS)
Conclusions and Challenges
Disaster Mitigation Workshop at APAN43 on 15-16 Feb 2017

## Slide 3
Source: Global Fire EWS--http://www.fire.uni-freiburg.de/gwfews/index.html & de Groot et al., 2010
Early Warning System for Forest Fire or Wildland Fire (EWS-Fire) is a system that will allow forest fire managers and related people to mitigate fire-related problems, to know fire fuel conditions, to reduce fire suppression costs and to enhance more efficient fire control. Forest and land management agencies, as well as land owners and communities, require early warning of extreme fire danger conditions that lead to uncontrolled wildfires.

## Slide 4
Fire danger rating (FDR) is a mature science and has long been used as a tool to indicate the potential of fire start, spread and impact. Fire danger rating is the systematic assessment of fire risk and potential impact, and it is the cornerstone of contemporary fire control and management program.
Source: Global Fire EWS--http://www.fire.uni-freiburg.de/gwfews/index.html & de Groot et al., 2010
Wagner, V., 1987

## Slide 5
Fire Danger Rating System (FDRS):
  Use weather data at noon as inputs (Van Wager, 1987, Lee et al. 2002, Amiro et al., 2004, de Groot et al., 2006, Taylor and Alexander, 2006 and FAO, 2006)
  Temperature
  Humidity
  Wind Speed
  Amount of 24 Hours Precipitation
  CFFDRS software can be downloaded at http://www.lakestatesfiresci.net/SciLibrary/FireDanger.htm and http://rpackages.ianhowson.com/cran/cffdrs/man/fwi.html

## Slide 6
Fire Danger Rating information is used for many operational reasons:
to determine suppression resource levels (fire fighters, equipment, helicopters, fixed wing air tankers), mobilization, and strategic prepositioning;
to define safe and acceptable prescribed burn prescription criteria;
to establish fire management budgets based on long-term fire danger statistics; and
to justify increased funding during times of wildfire disaster.
Source: Global Fire EWS--http://www.fire.uni-freiburg.de/gwfews/index.html & de Groot et al., 2010

## Slide 7
FDRS History
  Began in U.S. in 1919; Canada in 1925; Russia in 1949
  In Canada began with field data collection of how trees were responded to fire
    Have a system in used in 1960
    in 1987 Van Wagner developed into a better easy to use system
Source: Wildfire Hazards, Risks, and Disasters, Ch. 11 Wildland Fire Danger Rating and Early Warning Systems, William J. de Groot, B. Michael Wotton, Michael D. Flannigan 2015

## Slide 8
new longer term predictions of fire danger based on advanced numerical weather models
common global fire danger metrics to support international fire management cooperation, including resource-sharing during times of fire disaster
a fire danger rating system for the many countries that do not have a national system in place
Source: Global Fire EWS--http://www.fire.uni-freiburg.de/gwfews/index.html & de Groot et al., 2010

## Slide 9
1. Long-term early warning products (or seasonal forecasts) provide an indication of anticipated global trends in fire danger over the course of the upcoming fire season.
2. Medium-term early warning products (1-2 weeks) provide information for large-scale tactical decision-making that requires 'spool-up' time to implement fire management action plans such as arranging the transfer of helicopters, fixed-wing air tankers, or fire fighters and equipment across international borders.
Source: Global Fire EWS--http://www.fire.uni-freiburg.de/gwfews/index.html & de Groot et al., 2010

## Slide 10
3. Short-term of 1-5 days provides information for strategic decision-making, such as pre-positioning suppression resources in the most critical areas to most effectively control new fires and contain on-going fires.
Fire danger is calculated with Global Forecast System data from the U.S. National Centers for Environmental Prediction (NCEP) or The European Centre for Medium-Range Weather Forecasts (ECMWF).
Source: Global Fire EWS--http://www.fire.uni-freiburg.de/gwfews/index.html & de Groot et al., 2010

## Slide 11
Source: http://www.fire.uni-freiburg.de/gwfews/index.html
Forecast fire danger provides early warning of future trends in fire potential, allowing fire managers to plan/implement fire control strategies in advance.

## Slide 12
ASEAN FDRS History
  El Nino 1997-8 caused severe smoke and haze problem in Indonesia and neighboring countries
  ASEAN signed agreement in 2002
  2002-2005 System Development through Canadian Forest Service support
  2006 started running the system at Malaysian Meteorological Department

## Slide 13
ASEAN System by Malaysian Meteorological Department
Source: http://haze.asean.org/#

## Slide 14
Source: http://haze.asean.org/#
ASEAN System by Malaysian Meteorological Department

## Slide 15
Source: http://www.met.gov.my/web/metmalaysia/climate/fdrs/southeastasia
ASEAN System by Malaysian Meteorological Department

## Slide 16
ASEAN System
Source: http://www.met.gov.my/web/metmalaysia/climate/fdrs/southeastasia

## Slide 17
http://www2.dnp.go.th/gis/FDRS/FDRS.php
http://haze.asean.org/fire-danger-rating-system-fdrs-for-southeast-asia/
Differences

## Slide 18
http://www2.dnp.go.th/gis/FDRS/FDRS.php
http://haze.asean.org/fire-danger-rating-system-fdrs-for-southeast-asia/
Differences

## Slide 19
http://www2.dnp.go.th/gis/FDRS/FDRS.html
Source: http://www2.dnp.go.th/gis/FDRS/FDRS.php
Manomaiphiboon, K., Tanpipat, V., Nhuchaiya, P., Jaroonrattanapak, N., 2015

## Slide 20
Combining forecasted fire danger maps with historical fire hotspots will indicate critical areas where serious fire problem will occur if current fire activity persists.

## Slide 21
Using FWI with fire hotspots on Google Earth
2 October 2016

## Slide 22
สกลนคร

## Slide 23
6 Basic steps you have to do:
Prevention
Monitoring
Prediction (Forecasting, Modeling)
Warning
Response
Recovery, Assessment, Mitigation
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 24
Prevention
  Rising Awareness through
    Public Relation and Propaganda
    Training
    Fire break activities with locals
  Community Based Fire Management (CBFiM)
  Etc.
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 25
Prevention

## Slide 26
Prevention

## Slide 27
Monitoring
  Watch-out tower, different vehicles (car, SUV, motorcycle, and bicycle), helicopters, fixed wings, EOS, UAV (unmanned aircraft vehicle), CCTV with both visible and thermal infrared camera
  Public Network
  Etc.
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 28
Monitoring tools
1362
Public Report

## Slide 29
HKK Wildlife Sanctuary

## Slide 31
CCTV System
Source: http://www.fire.uni-freiburg.de/iffn/country/pt/pt_4.htm

## Slide 32
Thermal and Visible Camera
Source: http://www.insightrobotics.com
Source: http://hopewish.en.made-in-china.com/product/AqkmbTocYwUf/China-Fire-Alarm-System-Thermal-Imaging-Camera.html

## Slide 33
Unmanned Aircraft Vehicle
Source: https://www.icarus.upc.edu/ en/research/unmanned-aerial-systems-uas

## Slide 34
Source: http://www.interpine.co.nz/news/default.aspx
UAV

## Slide 35
EARTHDATA Fire Information for Resource Management System
Source: https://firms.modaps.eosdis.nasa.gov/

## Slide 36
Source: https://worldview.earthdata.nasa.gov/

## Slide 37
Flow Chart of Thailand Fire Danger Rating System and Fire Hotspot

## Slide 38
Daily report to the main forest fire control task forces by using rapid and daily fire hotspot alert emails, www FDRS, and a smart phone applications (e.g. LINE) by Department of National Park, Wildlife and Plant Conservation (DNP)
Where?
Which forest fire control responsibility!
A Daily Report by DNP
Source: http://portal.dnp.go.th/

## Slide 39
Chiangrai Hotspot & Early Burning Application
Sirimongkonlertkun, N. and Yanawongsa, E., 2016

## Slide 40
Monitoring Transport of Biomass Burning Aerosols
Himawari-8 Geostationary Monitoring
http://www.highfirerisk.com.au/imr/Thai_H8_01.htm
http://www.data.jma.go.jp/mscweb/data/himawari/sat_img.php?area=se1
http://realearth.ssec.wisc.edu/
Rick McRae, Risk Analyst, Emergency Management, Risk and Spatial Services, ACT Emergency Services Agency, Australia
Notes: Recent advances in the US (NRL/NOAA) NRT monitoring of fire aerosols

## Slide 41
Prediction (Forecasting and Modeling)
  Smoke and haze monitoring and forested system (7 SEAS and ECMWF-CAMS, Himawari-8)
  Early Warning System for fire (EWR-Fire) based on Fire Danger Rating System (FDRS) such as GFEWS, EFFIS, UATFFDRS, INFFDRS
  Etc.
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 42
Smoke and Haze Monitoring By 7 SEAS
Source: http://www.nrlmry.navy.mil/aerosol_web/7seas/7seas.html
Notes: Recent advances in the US (NRL/NOAA) NRT monitoring of fire aerosols

## Slide 43
Forecasted Smoke and Haze By 7 SEAS
Aerosol Optical Depth
24-30 April 2016
Source: http://www.nrlmry.navy.mil/aerosol_web/7seas/7seas.html
Notes: Recent advances in the US (NRL/NOAA) NRT monitoring of fire aerosols

## Slide 44
Forecasted Smoke and Haze By 7 SEAS
Source: http://www.nrlmry.navy.mil/aerosol_web/7seas/
18-22 April 2016
25-29 April 2016
Notes: Recent advances in the US (NRL/NOAA) NRT monitoring of fire aerosols

## Slide 45
Fire Radiative Power – Aerosol Optical Depth
by Copernicus Atmosphere Monitoring Service (CAMS) and
Copernicus Climate Change Service (C3S), implemented by ECMWF.
Source: http://macc.copernicus-atmosphere.eu/d/services/gac/nrt/fire_radiative_power!SE%20Asia!Fire%20Radiative%20Power!macc!od!enfo!fire_radiative_power!2017020700!/
Source: http://www.gmes-atmosphere.eu/d/services/gac/nrt/nrt_opticaldepth!03!Total!SE%20Asia!macc!od!enfo!nrt_opticaldepth!2016121400!!/
Notes: Recent advances in the US (NRL/NOAA) NRT monitoring of fire aerosols

## Slide 46
Source: http://www2.dnp.go.th/gis/FDRS/FDRS.php/
Forecast Fire Danger Rating for Upper ASEAN and Thailand

## Slide 47
Warning FIRMS active fire or fire hotspot alert emails:
  Review historical fire related by EOS directly in WorldView for overall situation
  Forecast Fire Danger Rating System (FDRS)
  Risk maps
  Daily fire fuel survey
  Weather condition
  Fire Radiative Power
  Etc.
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 48
Smoke and haze caused by fires in Maechaem area during 16 – 24 April 2016
16 April
19 April
22 April
17 April
18 April
20 April
21 April
23 April
24 April
Source: https://worldview.earthdata.nasa.gov

## Slide 49
Fire Weather Index
Source: http://www2.dnp.go.th/gis/FDRS/FDRS.php/

## Slide 50
Source: http://www.cefa.dri.edu/CFS/fwi.php and : http://www.fire.uni-freiburg.de/gwfews/forecast_ews.html
New calibrated Thresholds being used by Global Fire EWS for upper ASEAN (Bill De Groot & Alan Cantin, Natural Resources Canada, Canadian Forest Service) with Global FWI Monthly Forecast for 9 Months for Planning Prescribe Burning and Others

## Slide 51
Source: http://forest.jrc.ec.europa.eu/effis/applications/global-viewer/
Global Wildfire Information System by The European Forest Fire Information System (EFFIS)

## Slide 52
  Weather (wind, precipitation, etc.)
    Windyty (http://www.windyty.com)

## Slide 53
Source: http://www.gmes-atmosphere.eu/d/services/gac/nrt/fire_radiative_power/
Fire Radiative Power
Mark Parrington, ECMWF, 2017

## Slide 54
Response
  Forest fire suppression units
  Related agencies and collaborated local communities
  Etc.
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 56
Recovery, Assessment and Mitigation
  Burn Severity Index (BSI)
  Burn Area
  Emissions
  Reforestation
  Public Relation
  Etc.
What we need to cover in order to deal with Natural Disasters, especially forest fires?

## Slide 57: Burned Areas Detection using Burn Severity Index (BSI)
Ken Brewer and Carl Albury, 2015

## Slide 58
Source: http://apps.ecmwf.int/datasets/data/cams-gfas/
Source: http://www.globalfiredata.org/index.html
Emissions

## Slide 59
Fire Decision Support System (FDSS)
RS
ICT
GPS
GIS
FDSS
Socioeconomics, social dimension
maps, statistics, weather, models, topographic maps
EOS imageries, weather, climate, monitoring, detection, condition,
Communication technologies, related information & knowledge (research, publication,
Location identifying technologies, accuracy, GNSS

## Slide 60
Source: http://cwfis.cfs.nrcan.gc.ca/home

## Slide 61
  Conclusions and Challenges
  Need to combine and integrate Lower and Upper ASEAN FDRS together in order to complete the SEA regional picture
  Need to put fire early warning (Forecast FDRS) information into a forest fire planning process and daily forest fire control activities
  Need to develop better accuracy high resolution medium range weather forecast inputs (DA and Ensemble) for FDRS
  Need to have reliable and scientific proved Fire Decision Support System (FDSS) e.g. CWFIS
Disaster Mitigation Workshop at APAN43 on 15-16 Feb 2017

## Slide 62
  Conclusions and Challenges
  Need a full cooperation and supports from ASEAN forest fire agencies, people and related
  Need to accept, in Asia, the main cause of fires is “Human,” all advance information or system will mean nothing if we do not solve the real cause, so NEED to make people realize and concern how worse the smoke can do to them and their families!!!!! Moreover, need to provide other without fire alternatives for them to earn a living!
  Need to find easier and simpler communication schema to deliver scientific information.
Disaster Mitigation Workshop at APAN43 on 15-16 Feb 2017

## Slide 63
Acknowledgements
Dr. Jeff Schmaltz (NASA/GSFC-LANCE-Rapid Response),
Dr. Diane Davies (NASA-LANCE Operation Manager),
Prof. Dr. Johann Goldammer (GFMC, U. of Freiburg),
Dr. Robert Field (Columbia University, NASA GSFC),
Dr. Bill De Groot (NRCAN-Canadian Forest Service),
Mr. Rick McRae (ACT Emergency Services Agency),
Ms. Minnie Wong (WorldView, NASA-EarthData),
Ms. Anja Hoffmann (GOLD-GOFC Coordinator),
Dr. Jeff Reid and Dr. Edward Hyer (Naval Research Laboratory),
Dr. Mark Parrington (ECMWF)
Dr. Kaseamsan Manomaipiboon (JGSEE),
Dir. Siri Akkakara, Dir. Manus Panmon, Dir. Suraphol Leerawaropat (DNP), Mr. Prayoonyong Nuchaiya and Mr. Narin Jaroonrattanapak (DNP)
Disaster Mitigation Workshop at APAN43 on 15-16 Feb 2017